# Text boxes

Do Not:

---Allow the pressure inside the tank to exceed the MAWP (Maximum Allowable Working Pressure).

---Remove, plug or alter the safety relief valve setting.

---tamper with the pressure controls.

---Bump or dent the air tank.

---Install the tank on a foundation without vibration dampers.

---Shut the automatic condensate drain.

---Operate the Air Tank with an expired inspection certificate.

---Impart excessive loading on the Air Receiver components.

KEEP YOUR BOILER ROOM SAFE

Compressed Air Tanks

Objective: To educate the public on the safe and proper use of Unfired Pressure Vessels containing Compressed Air.

DLLR

Division of Labor and Industry

Boiler Safety Inspection Unit

1100 North Eutaw St, Room 605

# Baltimore, Maryland 21201

410-767-2330

boilers@dllr.state.md.us

www.dllr.state.md.us/labor/safety/boil.shtml

Lawrence J. Hogan

Governor

## Boyd K. Rutherford

Lt. Governor

Kelly M. Schulz

Secretary

We are here for your protection.

An Air Receiver is probably the most common type of unfired pressure vessel.

However, due to minimum size inspection thresholds employed by the State of Maryland, many of the smaller air receivers will not qualify for a mandatory in-service inspection.

The typical inspection threshold sizes in jurisdictional regulations are 5 cubic feet and 250 psi, or 1.5 cubic feet 600 psi.

Air receivers shall be constructed in accordance with ASME BPV Code Section VIII and are stamped with the ASME “U” or “UM” symbol.

Do---

---Drain the Air Tank daily of moisture to prevent internal corrosion .

---Install a safety valve set at or below MAWP and sufficient relieving capacity.

---Install a pressure gauge

- Keep your Boiler Room clean.

- Keep a check on leakages and rectify without delay.

- Don’t store flammables in the Boiler Room.

- In case of emergency, remain calm and use the emergency devices .

- In case of fire operate Emergency cut off switch.

- Maintain a Boiler Operation Log.

- Keep the Boiler Room ventilated

Do---

Have the air receiver  inspected biennially, as required by State Law.

Report to the Chief Boiler Inspector for the air receiver to be installed, at least 30 days prior to installation.

Test safety relief valve and log the tests.

Inspect the air receiver daily for proper operation.

Allow only authorized (“R” stamp holder) repair firms to make weld repairs.